1. Cut Steel
- Tubes, 2 ea: 1/4” x 6” x 12” x 26” long
- Angle iron, 10 ea: 27” per frame diagram
- Angle iron 1/4” x 2” x 2”, 2 ea: 4”, 1 ea: 2”, 2 ea: 8”
- Flat steel, 1/4” x 6”: 1 ea: 6”, 4 ea: 12”
- Flat steel, 1/4” x 8”: 13.5”
- Flat steel 1/8” x 4”: 1 ea: 14”, 2 ea: 1”
- 1 ½" x 2” pipe coupling: cut in half
- 1” engine shaft: cut in half
- 3/4” 11 tooth spline shaft: cut in half

---
2. Fabricate tanks
- Torch, then grind tubes and end plates
- Drill ½” holes for sight gauge
- Install sight gauge
- Weld flanges, pipe coupling and filler neck
- Weld end plates on tanks
- Weld supports for engine & control panel
- Weld battery bracket to fuel tank and solenoid bracket to battery bracket
- Soap bubble test and re-weld if necessary
- Drill smaller 7/16” holes & tap ¼” NPTF
- Mask holes and paint

---
3. Shaft Coupling
- Cut couplings in half
- Preferably: Use lathe to turn down cut ends
- Insert plug into coupling halves
- Clamp and weld
- Let cool standing vertically
- Paint external surfaces

---
4. Weld Frame
- Note: Mitered joints welded on inside and outside
- Begin in one corner, lay two members on flat surface, clamp and weld
- Add third member, clamp and measure – verify parallel with opposing member and weld
- Add forth member, verify alignment and weld
- Complete second rectangle
- Weld hoist points to upper frame members
- Align fifth and sixth members on one rectangle and weld
- Align second rectangle to first, position tanks inside frame and complete frame welds
- Weld expanded steel to hydraulic reservoir
- Weld solenoid bracket to battery bracket
- Paint frame & tank surfaces that will be inaccessible later
- Weld tanks to frame

---
5. Engine/pump mount
- Torch & drill holes in engine & pump plates – verify that holes on engine plate match those on support brackets on tanks
- Weld angle iron to pump plate
- Mount pump on pump plate
- Mount engine on engine plate
- Insert key in shaft coupling and connect to engine
- Slide pump assembly to shaft coupling
- Place 4” spacers between pump & engine plates
- Tack angle iron to engine plate
- Remove spacers and weld
- Remove engine / pump assembly and paint

---
6. Fabricate Control Panel
- Torch, drill, file control panel holes to drawing
- For key switch hole, use switch while filing to test for proper hole size
- Weld throttle bracket to back side & drill bracket
- Paint
- Mount control panel components:
  - Quick couplers
  - Key switch
  - Throttle

---
7. Fabricate Wire Harness
- Cut wire:
  - 2 ea: 10” 2 ga red
  - 1 ea: 12” 2 ga black
- 3/8” copper tubing: 6 ea @ 1 ½”
- Align wires, cut and strip ends appropriately
- Crimp fan connectors on wires
- Crimp circular lug on wire for solenoid
- Crimp pins on wires and insert into connector
- On large gauge wires, begin on ends with single wire – flare ends of copper tubing, insert wire, flatten with hammer and drill
- Proceed to ends with multiple wires – flare, insert, flatten and drill
- Cut heat shrink tubing, install on cables with multiple wires and heat to shrink

---
8. Oil Cooler & Fan
- Put teflon tape onto elbow connector NPT threads
- Screw elbows into oil cooler
- Position oil cooler: elbows up and facing you
- Insert plastic brackets in fan
- Place fan on oil cooler – wires pointing left
- Insert plastic fasteners through oil cooler and plastic fasteners, then secure (use foam pads to protect fins)

---
9. Install Engine / Pump
- Hoist engine / pump
- Attach vibration isolators to supports on tanks – loosely tighten from underneath
- Lower engine into frame until mated with isolators
- With full weight on vibration isolators install and tighten nuts

---
10. Install Oil Cooler & Fan
- Slide oil cooler / fan in place – be careful not to damage cooler fins
- Loosely connect hydraulic hoses to oil cooler elbows
- Test alignment of hydraulic hoses and adjust elbows if necessary
- Install oil cooler/fan to expanded steel using rubber bushings and bolts

---
11. Install Control Panel
- Position control panel
- Connect and tighten hydraulic hoses between oil cooler and control panel
- Connect ¼” hose for “Tank Return” to control panel and tank using hose clamps

---
12. Wire Harness and Battery
- Mount solenoid to bracket
- Insert battery in place
- Plug key switch connector to switch
- Plug in fan connectors
- Connect wire lug to solenoid
- Connect black battery cable to engine bolt and to battery
- Connect red cable to solenoid and engine
- Connect red cable to solenoid, then battery

---
13. Install Suction Plumbing
- Use teflon tape on all NTP threads!
- Install tank strainer in tank
- Install 1” x 4” nipple in strainer
- Install 1” elbow on nipple
- Install suction hose with 2 ea hose clamps

---
14. Install Supply Plumbing
- Use Teflon tape on all NPT threads!
- Connect “long” elbow to pump
- Connect ½” 1' hose between pump elbow and quick connect on control panel – minimize stress on hose
- Install ¾” nipple and filter head to tank – make sure fluid flow is into tank
- Install ¾” elbow in filter head
- Install filter on filter head
- Connect and tighten all ¾” JIC fittings

---
15. Fill With Fluids

---
16.Test