# Definitions
## Frame Tube Lengths & Hole Positions
- All frame members are 4” x 4” x 1/4” steel tube.
- Use the Frame Jig to mark matching holes on opposite sides of the tube.
- Drill each mark 13/16” (unless otherwise specified).
- Do not drill all the way through the tube from one side unless using a drill press.

Part	Illustration
Outer Base
Inner Base
Bottom Crossbar
A-Pillar
B-Pillar
C-Pillar
Top Crossbar
Cant Rail / The big hole at 46” should be / 2 3/8”. Use a cutting torch.
Power Cube Mount
Part	Illustration
Power Cube Mount / Holes 13/16 unless otherwise noted. The angle of the ramp needs to match the Power Cube. A good estimate is to leave a 3/4” gap between the top edge of the ramp and the top edge of the angle.
Hydraulic Valve Mount
Part	Illustration
Hydraulic Valve Mount / Additional holes for the hydraulic valves will be necessary. Use your specific hardware to mark the holes.
Loader Arm Crossbar Support
Part	Illustration
Loader Arm Crossbar Support
Base Cylinder Mount
Part	Illustration
Base Cylinder Mount
Loader Arm Cylinder Mount
Part	Illustration
Loader Arm Cylinder Mount / Drill out two nuts to 1” inner diameter and weld onto the 1” holes.
Loader Arm
Part	Illustration
Loader Arm / The big hole should be 2 3/8”. Use a cutting torch. The plug weld holes should overlap the lump when it is inserted into the end of the arm. Weld through the holes to secure the lump.
Loader Arm Crossbar
Part	Illustration
Loader Arm Crossbar
Loader Arm Insert
Part	Illustration
Loader Arm Insert
Tractor Frame Insert
Part	Illustration
Tractor Frame Insert
Loader Arm Lump
Part	Illustration
Loader Arm Lump / The top edges of the lump can be notched and rounded to better fit inside the loader arm tube.
Loader Arm Shaft
Part	Illustration
Loader Arm Shaft
Wheel Shaft Mount
Part	Illustration
Wheel Shaft Mount / The position and diameter of the four bearing mounting holes depends on the bearing block you end up using. Pictured is an example. / Use a cutting torch for the 2” shaft hole.
Motor Mount
Part	Illustration
Motor Mount / Use a cutting torch to make the large shaft hole. The motor mounting holes will depend on the particular hardware you end up using. This picture is just an example.
Motor Interface
Part	Illustration
Motor Interface / Use a cutting torch to make the large shaft hole. The motor mounting holes, if used, will depend on the particular hardware you end up using. The motor will probably be welded to this plate. This picture is just an example.
Wheel Hub
Part	Illustration
Wheel Hub / Use a cutting torch to make the shaft hole in the middle of the disc. The layout of the tire rim mounting holes will depend on the hardware you end up using. Pictured is just an example. / Gussets should be as close to 90* apart as possible.
Wheel Axle
Part	Illustration
Wheel Axle / Using a lathe, drill into the end of the axle shaft. Cut two slits on either side of the hole. Insert the smaller splined shaft and weld in place. Use the wheel hub to locate and drill a bolt hole through the other end of the shaft.
Quick Attach Plate
Part	Illustration
Quick Attach Plate
Pin
Part	Illustration
Pin / Weld a washer onto the end opposite the cotter pin hole.
Hardware
Power Transmission
Part	Illustration
Lock Collar / 1 7/8” / Double Split / https://www.surpluscenter.com/item.asp?item=1-2768-187&catname=powerTrans
Flange Bearing / 1 7/8” / 9/16” bolt holes / https://www.surpluscenter.com/item.asp?item=1-210-30-4&catname=powerTrans
Shaft Coupler / 1 1/4” bore / 5/16” keyway / https://www.surpluscenter.com/item.asp?item=1-1563-J&catname=
Splined Shaft / 1 3/8” / 6 teeth / https://www.surpluscenter.com/item.asp?item=1-2938-6&catname=
Female Splined Coupling / 1 3/8” / 6 teeth / https://www.surpluscenter.com/item.asp?item=1-1562&catname=
Hydraulics
Valves

Power Cube Delivery
Part	Illustration
Power Cube Delivery / Wrap all threads with teflon tape.
Power Cube Return
Part	Illustration
Power Cube Return / Wrap all threads with teflon tape.
Drive Control Valves
Part	Illustration
Drive Control Valves / Wrap all threads with teflon tape. / Cut off the tip of the power beyond sleeve just below the threads.
Cylinder Control Valves
Part	Illustration
Cylinder Control Valves / Wrap all threads with teflon tape.
Hoses
Part	Illustration
1/4”, 1/2” and 3/4” NPTM
Drive Power Hose
Part	Illustration
Drive Power Hose / Wrap all threads with teflon tape.
Drive Return Hose
Part	Illustration
Drive Return Hose / Wrap all threads with teflon tape.
Motor Drain Hose
Part	Illustration
Motor Drain Hose / Wrap all threads with teflon tape.
Power Cube Connection Hoses
Part	Illustration
Power Cube Connection Hoses / Wrap all threads with teflon tape.
Loader Cylinder Hoses
Part	Illustration
Loader Cylinder Hoses / Wrap all threads with teflon tape.
QA Plate Cylinder Hoses
Part	Illustration
QA Plate Cylinder Hoses / Wrap all threads with teflon tape.
Cylinders
Part	Illustration
Loader Cylinder / 2.5X36X1.5” / double acting / 3/8” NPT ports / https://www.surpluscenter.com/item.asp?item=9-6775&catname=hydraulic
QA Plate Cylinder / 2.5X30X1.25” / double acting / 3/8” NPT ports / https://www.surpluscenter.com/item.asp?item=9-7619-30&catname=hydraulic
Cylinder Fittings
Part	Illustration
Cylinder Fittings
Motor
Part	Illustration
Wheel Motor / 31.88 cubic inch / SAE 10 ports / SAE 4 case drain / https://www.surpluscenter.com/item.asp?item=9-7469&catname=
Motor Fittings
Part	Illustration
Motor Connections / Wrap all threads with teflon tape.
Valves
Part	Illustration
3-spool / spring centered / 3/4” NPT ports / 1/2” NPT ports / https://www.surpluscenter.com/item.asp?catname=hydraulic&qty=1&item=9-6761
2-spool / spring centered / 3/4” NPT ports / 1/2” NPT ports / https://www.surpluscenter.com/item.asp?item=9-6702&catname=hydraulic
Cushion Valve / 1/2” NPT / https://www.surpluscenter.com/item.asp?item=9-4019-50-H&catname=hydraulic
3/4” NPT check valve
Fittings
Part	Illustration
SAE 10M to 1/2” NPT nipple
SAE 10M to 1/2” NPTM swivel coupler
3/4” NPT nipple
3/4” NPTM 90 degree elbow
3/4” NPTF tee
3/4” female quick coupler
1/2” NPT quick coupler / Male and Female in one package
3/4” NPT power beyond sleeve / Cut off the tip of the sleeve just below the threads.
SAE 4M to 1/4” NPTM nipple
1/4” NPTM quick coupler / Male and female in one package.
1/2” NPT nipple
1/2” NPTF Tee
1/2” NPT swivel
1/2” NPT 90 elbow swivel
3/8” NPTM to 1/2” NPTF swivel
3/8” NPTM to 1/2” NPTF 90 swivel
1/4” NPT nipple
1/4” NPTF Tee
1/4” NPTF 90 elbow
3/4” to 1/4” NPT bushing