## Slide 1: Proposed OSE Reuse Exploration
Employing Widely Available Re-Usable Items:
Notes: OSE should look at reuse as part of its sustainability dictum. Here are some of my arguments.

## Slide 2: Some Very Common Items of Interest:
Intro: Our throw away society is awash with useful items sitting around in junk yards, back yards, barns, etc. Here are few of those items and suggested uses for the OSE sustainability efforts.
Pick Up Truck beds:
  Very strong robust mobile platforms that can readily be repurposed into tow behind trailers.
  I have one I want to experiment with as a mobile two axial solar trough tracker.
    Details later.
“C” Band Satellite Dishes 3M :
  These are wonderful solar collectors capable of generating enough heat to melt brick.
  They come in a variety of sizes and materials, the larger being more useful.
  My goal is to make them into two axial solar thermal collectors. I have qty(4) 3 meter dishes, that’s 12kW raw solar input.

## Slide 3: Common Items Cont’d
55 gal drums
  The Plastic variety can be used for:
    Rain Water collection
    Grain storage
    They have NPT 2” pipe thread so PVC connections can easily be made.
    Are mobile even when filled with water ~ 473 lbs. Two guys and a hand truck can move one.
    Can be obtained from food processors for $5.00 - $10.00 a pc.
  The Steel variety can be used for:
    Storing fuel
      bio
      petrol
      oil for lubrication
      cooking oil
    Can be modified into fuel tanks via the threaded openings.
    I plan to do experiment and turn a few into solar trough collectors.

## Slide 4: Common Items Cont’d
250/275 gal IBC Totes (Bulk Water Tanks)
  Are used for Aquaponics Tanks
  Purchased mine for $50.00 per unit.
High Efficiency Small Car Engines:
  There are cults built around small car engines. Three that come to mind:
  VW TD / TDI series 65 to 85 HP, four cylinder 1.6l - 1.8l diesels
  VW bug engines ranges of HP vary greatly
  Isuzu three cylinder, 55 hp, gasoline engines (of Geo Metro fame)
  All of the above engines have huge aftermarket supply chains
  Easily adapted to other purposes
  Worldwide Knowledgeable Users Groups
I have a VW TD 1.6l and an Isuzu 1.0l I’d like to integrate into a power cube design.

## Slide 5: Common Items Cont’d
Discarded Ornamental Iron
  Myriad of mild steel structural uses with the help of a welding machine and cutting torch.
Car / Truck Alternators
  Bosch built units internals are very robust and typically only need a charge controller replacement. Suitable diode rectifier circuitry could easily be designed and constructed by most techies.
  Are belt driven and are easily integrated into mechanical driven power applications.
Add your favorites here:

## Slide 6: Conclusion:
These are but a few extremely common items that literally litter the countryside. They are cheap, strong, easily modified and can be found in most places. And anyone mechanically inclined has plenty of experience with them.
By using commonly discarded useful items, costs can be reduced and build times reduced. Indentifying reusable items of high value and integrating their myriad uses into the OSE model will be a win / win..
I look forward to other suggestions to this list.