Circuit Explanation:

CLK: This is produced using an independant crystal oscillator and will need to operator at two times [ 2 x] the selected operating frequency. Oscillator will be chosen to operate at the N x 100kHz level, where N is between 1 & 5. Such a high frequency is selected in order to make the transformer core as compact as possible. Also, by having a dedicated crystal for the main PWM signal, the system can be made to have adjustable power levels dependant upon CLK frequency and limited by maximum MOSFET switching speed and core size. I contemplated directly producing the PWM signal from the arduino however this would have created problems due to the needed control code interfering with the continuous PWM signal. A second microcontroller could have been used however this seemed wasteful to use a complete controller for a simple operation.

PWM Circuit: The clock signal is fed into an integration circuit to produce a triangle wave which is then compared to a 0 to 5V control signal from an arduino in order to produce the needed adjustable PWM signal. A good explanation of the circuit can be found here: http://pcbheaven.com/circuitpages/Voltage_Controlled_PWM_Generator/

PWM SIGNAL CONDITIONING: A ‘D’ type flip flop is used in conjunction with an AND gate to ensure every other PWM pulse is used to create either the Positive or Negative half cycle and not both at the same time.

FET GATE DRIVERS: This part of the schematic is used to take the relatively weak control signal and boost it in order to push the FET’s on and off as quickly and safely as possible. Each driver can only handle one FET per channel, hence the need for one driver for every pair of FET’s.

FEEDBACK and CONTROL: Not shown on the schematic is the controlling arduino. Feedback is taken from the 170VDC output voltage, scaled down through an isolating phototransistor to 2.5V and fed into the arduino’s analog input. 2.5V is chosen as it aligns with a %50 duty cycle and if the output voltage raises or lowers due changes in load the feedback signal will change proportionally. A digital control scheme was chosen to allow for implementation of easily manipulated PID control loop schemes. The control signal is produced by taking a second PID controlled PWM signal through a low pass filter and feeding it to the main PWM circuit.

POWER ELECTRONICS: The Positive and Negative half cycle drive pulses are used to operate the Full-Bridge converter which takes the 72VDC battery voltage and produces a very high powered square wave. This 72V square wave is then stepped up through the transformer to a 170V square wave which is rectified and filtered to produce the needed 170VDC source voltage for the inverter. Any variance in desired output voltage due to switching, transformer core or load losses is taken into account by adjusting the PWM drive signals as needed.

PARTS:
Note: These are the only parts I have chosen thus far, all other parts shown in the schematic are place holders only and will not be the final component.

Power MOSFET: NTP5404NRG, low ‘on’ resistance, comes in thru hole package, high power capabilities

Gate Driver: NCP5181, able to drive high FET capacitances at high switching frequencies, built-in fixed propagation delay.